## Slide 1: Section 11: Cleaning, Disinfection and Sterilisation

## Slide 2: Key Definitions
Cleaning
  ‘removes dirt, grease, organic matter and micro organisms from a surface or item’
Disinfection
  ‘reduces/destroys micro organisms to a safe level’ - reduces the number of micro organisms
Sterilisation
  ‘Destroys all their micro organisms and spores’ – renders a surface/item free from all living organisms.
Without prior cleaning, disinfection and sterilisation will NOT be effective - Why?
Notes: Removes microorganisms and organic matter that maybe protect micro organisms or in the case of disinfection deactivate the disinfectant.

## Slide 3: Associated definitions
Detergent: A product that dissolves and removes dirt and grease
Sanitiser: A product that removes dirt and grease and reduces microorganisms to a safe level
Disinfectant: A product that reduces microorganisms to a safe level
Antiseptic: A substance that kills pathogenic microorganisms
Sterile: Free from microorganisms and their spores
Sterilant: A product that destroys all microorganisms and their spores
Aseptic: A procedure used to avoid the introduction of pathogenic organisms into the body site or onto an invasive device

## Slide 4: How do we achieve these processes in Special Procedures?
Cleaning
  Physical action
  Detergents/degreasers
  Ultrasonic cleaners
Disinfection
  Chemical
  Heat/thermal
Sterilisation
  Steam under pressure (autoclave)
  Cold sterilisation?
Notes: Colour coded equipment
Detergent and water
Detergent wipes
Drying
No sweeping brushes
Damp dust
Cleaning schedules

## Slide 5: Ultrasonic cleaning
Operate using a process called cavitation – bubbles are generated that vibrate within the liquid bath, attacking every surface including recessed and hollow areas
Items must be submerged in the detergent, then rinsed and dried using a clean, disposable towel.
Periodic testing of the machine is required
Machine should be used in accordance with manufacturers instructions
This is an efficient method of cleaning instruments and small pieces of equipment.

## Slide 6: Disinfectants - Examples

## Slide 7: The decision to clean, disinfect or sterilise is based on the risk of infection
Discuss which surfaces, equipment and instruments in a special procedures environment should be routinely:
Cleaned
Disinfected
Sterilised

## Slide 8: When would you disinfect a floor or walls?
Clean | Disinfect | Sterilise
Floors | Client chair/couch | Invasive equipment
Walls | Work station surfaces | Needles
Bins | Hand contact surfaces | Jewellery
Ceilings | Non invasive equipment | Ink/pigment
Clean, disinfect or sterilise?

## Slide 9: Risks of infection determine whether cleaning, disinfection and/or sterilisation is required
HIGH
  Anything that enters a normally sterile body area or is in contact with a break in the skin or mucous membrane
MEDIUM
  Anything in contact with intact mucous membrane
LOW
  Anything in contact with intact skin
MINIMAL
  Items not in close contact with people or their immediate surroundings

## Slide 10: Equipment: Disinfection, sterilisation or single use

## Slide 11: Barrier precautions – in addition to cleaning and disinfection
Notes: Covering a client chair with cling film – does this create another infection risk?
Possibly creates an ideal environment for microbial growth? Warmth/food/moisture/time

## Slide 12: Sterilisation intended for re-useable items used to pierce a person’s skin/come in contact with broken skin
Items include – clamps, forceps, jewellery, grips, tubes
Non-vacuum autoclaves – solid unwrapped instruments
  Sterilised items remain sterile for 3 hours or until the door is opened
Vacuum autoclaves – hollow or wrapped items
  Items are sterilized in a vacuum steam steriliser (with a drying cycle) Type S or N
  sterilised items that are wrapped will remain sterile as long as the wrapping remains in tact and dry

## Slide 13: Autoclaves
Vacuum autoclaves
  Use in accordance with manufacturers instructions
  Install, commission, validate and maintain in accordance with manufacturers instructions
  134°C for 3 minutes
  Use distilled or sterile water
  Daily checks and weekly testing required

## Slide 14: Sterilisation and autoclave use
Notes: What about ‘cold sterilisation’? And of course ‘single use sterile’ instruments –needles are a solution to using autoclaves

## Slide 15
Designated equipment sink
Ultra-sonic water bath
Vacuum autoclave
Sterilized equipment
Decontamination
& Sterilisation of re-useable equipment
Verification strips

## Slide 16: Common problems/compromises
Dilution rates and contact times
Incorrect application e.g. an aerosolised spray used to clean/disinfect a work surface
Manufacturers instructions not followed
Poor maintenance of equipment
Post contamination/cross infection
  Needs to be a clear flow from ‘dirty’ to ‘clean’
  Designated storage area
  Cleaning equipment cleaned and disinfected

## Slide 17: Poor practices associated with re useable equipment/instruments
Rinsing with boiling water
Antibacterial wipes
UV Boxes
Glass bead sterilisers and dry heat sterilizers
Barbicide soaking
General lack of awareness on decontamination & sterilisation stages

## Slide 18: Cleaning Schedules National Colour Coding Scheme
Scheduled cleaning
‘Clean as you go’
2 stage cleaning

## Slide 19: Cleaning schedule
Usage | Dilution of stock solution | Example dilution | Available Chlorine | 
 |  |  | % | Parts per Million (PPM)
Blood Spillages | 1 in 10 | One part hypochlorite to 10 parts water, e.g. 10 ml hypochlorite in 100ml water | 1.0 | 10,000
Environmental Disinfection | 1 in 100 | One part hypochlorite to 100 parts water, e.g. 10 ml hypochlorite in 1000ml (1 litre) water | 0.1 | 1,000
Should include the following:
Who?
What?
Where?
When?
How?

## Slide 21: Summary (1)
Cleaning. Disinfection. Sterilisation.
  Detergent
  Disinfection
  Santiser
  Sterilant
Autoclaves (vacuum and non vacuum) 134°C for 3 mins
Ultrasonic cleaners
Contact times and dilution rates
2 stage cleaning
Manufacturers instructions!

## Slide 22: Match the correct answer to the sentence
Question | Answer
Disinfectant | always follow the manufacturers instructions
Sterilisation | involves cleaning and disinfection
‘contact time’ refers to | clean at regular intervals
The purpose of a cleaning schedule is to | destroys all microorganisms and their spores
How can Practitioners make sure that a detergent is used properly? | the time that a substance should be left of a surface in order to work properly
Two stage cleaning | reduces micro organism to a safe level

## Slide 23: Answers
Question | Answer
Disinfectant | reduces micro organisms to a safe level
Sterilisation | destroys all microorganisms and their spores
‘contact time’ refers to | the time that a substance should be left on a surface in order to work properly
The purpose of a cleaning schedule is to | clean at regular intervals
How can Practitioners make sure that a detergent is used properly? | always follow the manufacturers instructions
Two stage cleaning | involves cleaning and disinfection

## Slide 24: True or False Quiz
Question | True or False
It is not necessary to clean a surface before applying a disinfectant | 
An ultra sonic cleaner can be used to clean and sterilise instruments | 
An autoclave uses steam under pressure to sterilise equipment | 
Non vacuum autoclaves are only suitable for wrapped or hollow instruments | 
Using an autoclave effective sterilisation requires equipment to be held at 134°C for 3 minutes | 
An ultrasonic cleaner uses sound waves to clean equipment | 
A cleaning schedule should include the frequency of cleaning, the product to be used, the method of cleaning and the person responsible for the task | 

## Slide 25: True or False Quiz - answers
Question | True or False
It is not necessary to clean a surface before applying a disinfectant | False
An ultra sonic cleaner can be used to clean and sterilise instruments | False
An autoclave uses steam under pressure to sterilise equipment | True
Non vacuum autoclaves are only suitable for wrapped or hollow instruments | False
Using an autoclave effective sterilisation requires equipment to be held at 134°C for 3 minutes | True
An ultrasonic cleaner uses sound waves to clean equipment | True
A cleaning schedule should include the frequency of cleaning, the product to be used, the method of cleaning and the person responsible for the task | True